## Slide 1: Geodatabase Design and Management Georeferencing & Editing

## Slide 2: For Any Project, Managing Data is Key
What stakeholders do you have to work with?
  What are their short term and long term needs?
  What data can you collect now to prevent going back to redoing the data collection

## Slide 3: For Any Project, Managing Data is Key
For your thoughts
  Think about what data you need to collect
    Do you want a user to manually enter the data or do you want coded values (Domains)?
      Will help in painting a clean dataset
    How many characters are needed for manually entered data?

## Slide 4: 11 Steps to Designing Geodatabases
Identify the information products you will create and manage with your GIS
Identify the key data themes based on your information requirements
Specific the scale ranges and the spatial representation of each data theme at each scale
Decompose each representation into one or more geographic datums

## Slide 5: 11 Steps to Designing Geodatabases
Define the tabular databases structure and behavior for descriptive attributes
Define the spatial behavior, spatial relationships, and integrity rules for your dataset
Propose a geodatabase design
Design editing workflows and map display properties
Assign responsibilities for building and maintaining each data layer

## Slide 6: 11 Steps to Designing Geodatabases
Build a working prototype. Review and refine your design
Document your geodatabase design

## Slide 8: Steps to Create A Geodatabase
Real Easy
Right Click New -> File Geodatabase
Give it a Name

## Slide 9: Creating A Feature Class
Inside the File Geodatabase (or Feature Dataset) right click or file new, then Feature Class

## Slide 10: Creating A Feature Class
Inside the File Geodatabase (or Feature Dataset) right click or file new, then Feature Class
Enter a Name and Alias
  Alias can have spaces and actual name, name is how to save the data in your geodatabase
Pick you feature type
  Point, Line, or Polygon

## Slide 11: Creating A Feature Class
Define your attributes
For the example in class you will create a type text field
Once we get this part click next and then define the projection

## Slide 12: Creating A Feature Class
Define your attributes
For the example in class you will create a type text field
Once we get this part click next and then define the projection
We will use State Plane NAD 1983 New York West (US Feet)
Click Next Through the different screens

## Slide 13: Creating A Feature Class
Define your attributes
For the example in class you will create a type text field
Once we get this part click next and then define the projection
We will use State Plane NAD 1983 New York West (US Feet)
Click Next Through the different screens

## Slide 14: Creating A Feature Class
Define your attributes
For the example in class you will create a type text field
Once we get this part click next and then define the projection
We will use State Plane NAD 1983 New York West (US Feet)
Click Next Through the different screens

## Slide 15: Creating A Feature Class
Define your attributes
For the example in class you will create a type text field
Once we get this part click next and then define the projection
We will use State Plane NAD 1983 New York West (US Feet)
Click Next Through the different screens

## Slide 16: Building A Domain
Domains allow you to standardize the data
Right click in the database and Click Domains

## Slide 17: Building A Domain
Domains allow you to standardize the data
Right click in the database and Click Domains
Use the Domain View and Add a New Domain for Wetland Type (Make Sure to Save when you are done)

## Slide 18: Adding the Domain to Our Data
Right Click on our Layer
Go to Design then Fields

## Slide 19: Adding the Domain to Our Data
Right Click on our Layer
Go to Design then Fields
Click on Domain and then Select the Wetland Type
Click Save To Save the Changes

## Slide 20: Importing Data Into Your Geodatabase
Simple Import and Export Commands to move your data around

## Slide 21: Exporting Data Into Your Geodatabase
Simple Import and Export Commands to move your data around
Can create CAD, Shapefiles, and move to geodatabases
You will also notice an XML Workspace Document
This is a way to work with the database schema outside of ArcGIS

## Slide 22: Exporting your geodatabase Schema to XML
If you want to share the geodatabase schema that you just created you can create an XML Workspace
Using the XML a user can reconstruct the schema and even the geodatabase with just one step
To create the XML Workspace right click on your geodatabase
Then export Geodatabase to XML Workspace Document
Your Input will be the geodatabase
Save the output to somewhere you know and with a good name
Then set it to Schema only
  Data will export all of the data along with the schema

## Slide 24: Georeferencing
Georeferencing is using an unprojected image and using known landmarks in a GIS placing that image in its projected space
It is done through the Georeferencing Ribbon (found in the Imagery Ribbon)
You can use the toolbar to roughly fit the drawing to the space
You can use the add control points to help line up the data

## Slide 25: Georeferencing
One thing to always know, when adding control points always go from the image to the map to line up your data
You can use the Link Table to see your error
  For this example, your error should be very close to zero
  Many times your scanned image is not going to be as clean so you will need to get as low as possible, but about half the resolution is recommended
When you finish (more than 4 points) Click Save in the Georefrecing Ribbon and that will save the data to the image

## Slide 26: Editing
To create data you will need to use the Edit Ribbon
This can be found like any other toolbar or in the main menu as the pencil with some dots and lines
To edit you need layers to edit (the vector data you are working on)
The editor will activate when you specify the start editing command
Anything you do in an edit session will be temporary until you save your edits

## Slide 27: Editing
If you have your symboloy set before you start editing it will add it to your feature template
To add a new feature, click on the one you want to add and then draw it on the map
  To finish a line feature you can either double click or hit f2
Once you have a feature you can click on the attribute button and type in the attributes into the table

## Slide 28: Editing
To edit an existing feature, you can use the modify tool
Just single click to edit the attributes or double click to edit the geometry
Once you are done you will start to see your features appear on your map document

## Slide 29: Save Edits
Make Sure to Save Your Edits

## Slide 31: Data Creation Lab
This lab is 2 parts
Part 1 is a database creation and data management assignment. You will be making a GIS Layer for the Old RIT Masterplan (MPNatSys2.tif). To do this you will need to have a geodtabase setup with the required 3 feature classes (Wetlands, Buildings, and 1 layer of your choice) each with attributes, domains, and anything else needed. Your deliverable for this part will be the XML database schema and a brief writeup on your reasoning how you setup your third layer. Also in the writeup explain if there is enough information in the scan to populate the all of the layers in the database and if not where would you go to get it. Due November 4th
Part 2 is adding data to your geodatabase. You will have to digitize the wetlands, buildings, and the third layer of your choice with the attributes and domains you selected in part 1. Your deliverable for this part will be the project file (ppkx). Due November 18th

## Slide 32: Reminder How to Create the Project Package PPKX
Go to the share ribbon and then Project
Save the Package to file
Save the file
Give it a Summary and Tag
Then Package